## Slide 1: HVAC BEHAVIORAL RESEARCH INITIATIVE
Kristin Heinemeier PhD, Sarah Outcault PhD, Jennifer Kutzleb, Marco Pritoni, Michael Lingenfelter, Alan Meier PhD

## Slide 2: Overview
HVAC Behavioral Research Initiative, a few upcoming projects:
    The Role of Behavior in Emerging Technologies
    The Role of Behavior in ZNE Homes
    Field Study of Advanced Thermostats
Where are we going next?
Qualitative Research Methods

## Slide 3: THE ROLE OF BEHAVIOR IN EMERGING TECHNOLOGIES

## Slide 5
End user
Technology
“Middle Men”
Psychology
Sociology
Physiology
User Interface
Comfort Conditions
Accountability
Competence
Trust/Relationship

## Slide 6: One Barrier: Perceived Value and Technician Sophistication

## Slide 7: Case in Point: Economizers
Simple idea but very complex technology.
Many techs don’t understand them.
High-limit temperature setting is important, but not well understood.
Not visible and doesn’t affect comfort > not much attention
Easy to disable…up to 40% are disabled right now!
Greater than 60% failures in the field.

## Slide 8: Economizers Have a Very High Failure Rate
% Failure | Source | Notes
43% | AEC 2002. | Just damper faults.
50% | Mike Kaplan, Personal Communication with Dave Sellers, 1999. | New construction.
56% | HEC, 1993. | Economizers up to two years old.
64% | Jacobs and Higgins, 2003; and Jacobs et al., 2004. | 124 RTUs 10 tons or less, with economizers.
64% | Jonathan Woolley, Personal Communication, 2013. | 22 RTUs with economizers.
65% | Goody et al. 2003. | Small commercial RTUs.
66% | NEES, 1993. | Units two years old or newer
70% | Davis, et al. 2002. | Small number of RTUs.
70% | KEMA, 2013a | Economizers that had been fixed up to a year ago.
75% | Craig Hofferber, Personal Communication with Dave Sellers, 2000. | Estimate from interviews with consultants, mechanical contractors, and commissioning agents.
80% | Felts and Bailey, 2000. | Existing RTUs
100% | Pratt, et al., 2000. | Four of four RTUs investigated.
Source: Heinemeier, in press, ACEEE 2014

## Slide 9: Emerging Technology Studies
Advanced Digital Economizer Controllers
Fault Detection and Diagnostics
Climate Appropriate HVAC Systems

## Slide 10: THE ROLE OF BEHAVIOR IN ZNE HOMES

## Slide 11: E-Sogo Smart House

## Slide 12: Analysis of First Year Performance
Source: Tokyo Gas Company
Energy Efficiency Envelope and Architectural Design
On site energy system
36%
The primary energy
usage
70%
reduction
About 30%reduction

## Slide 13
UC Davis West Village
Objective: ZNE Complex
About 15% shy of goal
Consumption of different apartments varies widely… why?

## Slide 14
14
Comparison of Household Energy Consumption
Source: Jukankyo Research Institute
Notes: 14

## Slide 15: Task/Ambient Conditioning
Brazier
Kotatsu
Room-AC
Jukankyo Institute

## Slide 16: FIELD STUDY OF SMART THERMOSTATS

## Slide 17: Use of Default Schedules and Manual Operation
“Occupied” and “Unoccupied” settings still set at installation default temps and times of day, months after installation.
Room temperature managed manually, by teacher, using a “hold” feature in the wall thermostat.

## Slide 18: The Bottom Line
Participants felt:
    Angrier
    More powerless
    More bewildered
    More frustrated
    Less comfortable
    Less “In-control”
No Significant Energy Savings
Savings Depended on Prior Thermostat Use
Smart Defaults, Third-Party Setting Setpoints
Need for an Ultra Transparent Simple Thermostat
Site | Energy savings
Golf Clubhouse | +3.5% of HVAC power draw per degree F
Small Restaurant | -6.7% of HVAC power draw per degree F
Private School | Pending

## Slide 19: WHERE ARE WE GOING NEXT?

## Slide 20: Technologies to Improve the Effectiveness of Residential HVAC
Avoiding system use
          Task and Passive Cooling
Reducing system runtimes
          Thermostat Usability Extremes
Keeping systems working efficiently
          Ensuring Occupant or Service Provider Response to FDD Alarms
Optimizing system replacements
          Understanding the Role of the Middleman/Perception of Sophistication and Value

## Slide 21: QUALITATIVE RESEARCH METHODS

## Slide 22: Methods Used in Upcoming Studies
Study | Sponsor | Participants |  |  |  |  |  | Research Methods |  |  |  |  | 
 |  | Res |  | Com |  | Mfg,/Dist | Other | Surveys | Focus Groups | SS Interviews | Experiment | Monitoring | Observations
 |  | Owners/Tenant | Contr/Tech | Owners/Tenant | Contr/Tech |  |  |  |  |  |  |  | 
Behavior in Emerging Techs: Economizers | SCE |  |  | X | X |  |  |  |  | X |  |  | 
Behavior in Emerging Techs: FDD | SCE |  |  | X | X |  |  |  |  | X |  | X | 
Behavior in Emerging Techs: Climate Appropriate | SCE | X | X | X | X | X | Specifying Engineers |  | X | X |  |  | 
Behavior in ZNE Homes | Tokyo Gas | X |  |  |  |  |  | X |  | X |  | X | X
Market Intelligence | CPUC |  |  | X | X | X | Government, Utilities, Researcher, Consultant, NGOs |  |  | X |  |  | 
Market Transformation Indicators | CPUC |  | X |  | X |  | Consultants, Utilities, Evaluators | X |  |  |  |  | 
Market Assessment of Code Compliance | KEMA | X | X | X | X |  | Code Officials, HERS Raters | X |  | X |  |  | 

## Slide 23
What is “Qualitative Research”?
Who? What? When? Where? Why? How?
Behaviors
Emotions
Cognition
Physical
Social
Legal
Institutional
Environmental context

## Slide 24
What is it Good For?
Discovery
  Identifying themes and relationships
Description
  Understanding complex, dynamic multidimensional phenomenon
Comparison
  Group A vs. Group B
Explanation
  Relationship between sets of variables (causal or non-causal)

## Slide 25
How do we Ask People?
Unstructured
Structured
Informal interviews
Ethnographic interviews
Standardized
  e.g., surveys
Semi-standardized
  e.g., Focus groups
Semi-structured
Provide structure
Provide flexibility
Encourage detailed responses
Elicit different types of data
Elicitation techniques

## Slide 26
What Types of Questions can be Asked in a Semi-Structured Interview?
Lists
  “Why”
  Descriptions
Relations
  Compare & contrast people, space & time
  Frames
Processes
  Mechanisms
  “How”
  Descriptions of events

## Slide 27
Balance depth and breadth
  Allow us to efficiently collect and analyze rich, qualitative data from many respondents (not either/or)
Ensure consistent data collection across subjects and interviewers
Balance research objectives with resource constraints
  Answer complex research questions thoroughly and on budget (i.e., for less than a gazillion dollars)
What’s so Great about Semi-Structured Interviews?

## Slide 28
Why Can’t We Just do a Survey?
You have to know the answers to write the (narrow) questions
When we don’t already know the answers, we have to ask broader questions
  How do you calibrate your temperature gauges? (check one)
    __Send it to a calibration service provider
    __Use an ice bath and/or boiling water
    __Someone else does it
    __Other _____________________________
    __It doesn’t get done
  Describe the challenges you have promoting energy efficiency?
  Who? What? When? Where? Why? How?
We don’t know about Grandma.
That requires semi-structured interviews.

## Slide 29: Questions, Comments, Discussion
Thank you!

## Slide 30
How Can We do Semi-structured Interviews Efficiently (i.e., For Less Than a Gazillion Dollars)?
Develop logic model outlining the phenomenon of interest
Create semi-structured interview protocol
  Use structured data collection instruments
    Super cool “spy” pen
    Create note-taking table
    Build database
  Develop coding scheme to convert text to numbers
  Analyze data with qualitative and quantitative techniques

## Slide 31: Methods Used in Past Studies
Study | Sponsor | Participants |  |  |  |  |  | Research Methods |  |  |  |  | 
 |  | Res |  | Com |  | Mfg,/Dist | Other | Surveys | Focus Groups | SS Interviews | Experiment | Monitoring | Observations
 |  | Owners/Tenant | Contr/Tech | Owners/Tenant | Contr/Tech |  |  |  |  |  |  |  | 
Maintenance Behavior | SCE | X | X | X |  |  |  | X | X | X |  |  | 
Compliance Motivations | WHPA |  | X |  |  |  |  | X |  |  |  |  | 
Usability of In-Home Energy Displays | SCE | X |  |  |  |  |  | X |  |  | X |  | 
West Village Energy Use Behaviors | SCE | X |  |  |  |  |  | X |  |  |  |  | 
Tiny Steps/Feedback Test | Toyota | X |  |  |  |  |  | X |  |  |  | X | 
Technician Behavior | SCE |  | X |  |  |  |  |  |  | X |  |  | X
Prevalence of Faults in RTUs | WHPA |  |  |  | X |  |  | X |  |  |  |  |